## Slide 1: Multivariable control: constraint controllers

## Slide 2: Constraint controllers
drive the process towards operating limits
we want to profit as much as possible!
hard constraints
    approached from one side
    something might be mechanically impossible
    e.g. safety reasons, valve opening 0-100%
soft constraints
    approached from either side
    violating should not be a major problem
    e.g. non-hazardous liquid level (no overflow)
Notes: Constraint controllers are designed to drive the process towards operating limits in a direction known to be profitable. Constraints are either hard or soft.
Hard constraints are those which can only be approached from one side. This might be because it is mechanically impossible - for example, a control valve cannot open beyond 100%. Or it can be imposed for safety reasons - for example operating pressure can be theoretically increased above a relief valve setting but doing so would be extremely hazardous.
Soft constraints can be approached from either side. Violation of a soft constraint does not give a major problem, provided corrective action is taken promptly. Example is liquid level - while low and/or high limits may be set, these may be violated briefly with no impact on the process.

## Slide 3: Constraint controllers
Single-input single-output (SISO) controllers
    one MV, one constraint
Multi-input single-output (MISO) controllers
    one MV, multiple constraints
Multi-input multi-output (MIMO) controllers
    multiple MVs, multiple constraints
Notes: Constraint controllers fall into three categories:
- Single-input single-output (SISO) controllers - they can manipulate only one manipulated variable (MV) to approach only one constraint.
- Multi-input single-output (MISO) controllers - they’re required when there is more than one constraint that is approached by adjusting just one manipulated variable (MV). Such controllers require some form of logic to select the most limiting constraint. Once selected the controller behaves just like SISO controller.
- Multi-input multi-output (MIMO) controllers - they adjust multiple manipulated variables (MV) to satisfy multiple constraints. It permits some simple economics to be defined by the engineer to drive the controller to select the most profitable set of constraints to approach. This establishes the desired conditions (SPs).